## Slide 1: Detecting Neutrinos via Active Radar Sounding
Richard Moser,
The University of Kansas
Notes: Richard Moser
Working with
Dr. Dave Besson at KU
Dr. Dave Seckel at the University of Delaware for the last 6 weeks at the first year of the IceCube summer program

## Slide 2: Neutrinos
Smallest known particle with mass
The only known particle that can reach the us unattenuated
  Chargeless – do not interact magnetically
    This means that they point back to their origin
  Interact very rarely
    Likelihood of interaction increases with energy
    i.e. innumerable neutrinos are passing through all of us right now as if we weren’t here.
Notes: Neutrinos do interact gravitationally, making them a possible candidate for dark matter

## Slide 3: Current detection methods
Optical: Icecube – detects Cherenkov radiation in the ice at the South Pole
  Requires the Cherenkov light cone to actually “strike” the light sensors
  Limits the minimum density of the detector
Radio: ANITA – detects Askaryan radiation via a floating/flying antenna array above the South Pole
  Also requires RF signal to “strike” the antennas
  Antenna array is functionally one point
    Provides a bearing and an angle but not a full “track” of the particle
And several more
Notes: Antarctic Impulsive Transient Antenna

## Slide 4: IceCube source: https://icecube.wisc.edu/science/icecube/ ANITA source: https://www.phys.hawaii.edu/~anita/campaigns/anita-ii

## Slide 5
Notes: As a quick review, in the energy spectrum of neutrinos, there exists a gap in our current capabilities to effectively detect Ultra High Energy neutrinos. The active radar sounding method offers a chance to peel back the curtain and illuminate this energy range.

## Slide 6
Notes: UHE ≥ 1016 eV
Limiting factor of IceCube on the high end is flux or number of neutrinos per cubic unit of area. The energy is great enough that Icecube can see it but only if the neutrino hits the bullseye that is the detector.

## Slide 7
Notes: UHE ≥ 1016 eV

## Slide 8: The case for active radar emission based neutrino detection methods
“Sir, you were going 6.706e8 in a 35”
Notes: How do we detect these ultra high speed particles? We almost need to set up a speed trap

## Slide 9: RADAR - RAdio Detection And Ranging
Requirements: Transmitter, target, and receiver

## Slide 10: Neutrino Particle Shower Plasma
“As these shower particles traverse the interaction medium, they eject cold ionization electrons from atoms in the bulk, forming a tenuous particle-shower plasma (PSP), distinct from the energetic shower front particles responsible for ionization. For high incident particle energies (E ≥ 1 PeV, consistent with, and beyond, the experimental reach of the IceCube[1] experiment), this plasma will become dense enough to reflect incident radio-frequency (RF) radiation”
Notes: This is the cardinal sin of powerpoint and I apologize. I leave it here in case anyone wants to read the full thing.
Greater than 1 PeV? Where have we seen that before?

## Slide 11
Notes: At PeV and higher energies, the plasma becomes dense

## Slide 12: Example detector
Observation of Radar Echoes From High-Energy Particle Cascades
  S. Prohira, K.D. de Vries, P. Allison, J. Beatty, D. Besson, A. Connolly, N. van Eijndhoven, C. Hast, C.-Y Kuo, U.A. Latif, T. Meures, J. Nam, A. Nozdrina, J.P. Ralston, Z. Riesen, C. Sbrocco, J. Torres, S. Wissel: 2019
  https://arxiv.org/abs/1910.12830

## Slide 13: Effective array volume
Observation of Radar Echoes From High-Energy Particle Cascades
  S. Prohira, K.D. de Vries, P. Allison, J. Beatty, D. Besson, A. Connolly, N. van Eijndhoven, C. Hast, C.-Y Kuo, U.A. Latif, T. Meures, J. Nam, A. Nozdrina, J.P. Ralston, Z. Riesen, C. Sbrocco, J. Torres, S. Wissel: 2019
  https://arxiv.org/abs/1910.12830

## Slide 14: Advantages of active emission
Received signal strength scales with transmitter signal power, not just particle energy
Indirect particle detection
  The “plane” doesn’t have to hit the reciever for the reciever to see it
Greater detection range = lower sensor density = larger array
Better anthropogenic and background noise rejection
  Received signal should closely match transmitted signal
    Continuous CW pulse – from transmitter in shadow zone
Active detection sensitivity should peak in the 10-100PeV range where other sensors are less effective
Notes: The nice thing about radar is that the reflected signal you get back should be roughly the same as what you transmitted, it is the transformations to that signal that give you information about what they were reflected off of.

## Slide 15: Radio Scatter
C++ over ROOT radio/particle simulation software
Used to simulate incident radio frequency Radiation from a particle shower and scattered signal
  i.e. simulates shooting high speed plasma with a radar gun
Calculates with regard to and allows testing of:
  Transmitter, particle, & reciever geometries
  Antenna gain
  Refraction properties in the medium (ice)

## Slide 16: Early results
Notes: On the left we see a clean, noiseless waveform reflected off of the digital plasma from the shower shower. On the right is a spectrogram which shows a wide swath. Oddly the swath starts at about 37 nanoseconds while the waveform pulse begins around 50ns from t-zero

## Slide 17: The ideal return
Particle-level model for radar based detection of high-energy neutrino cascades
  S Prohira, D Besson: 2017
  https://arxiv.org/abs/1710.02883
Notes: In the radio talk a week ago I asked if this was even a useful way to plot the data. This is a prettied up plot of a better return. Notice that the waveform shows noise but the received signal rises out of it nicely. In the spectrogram, the chirp shows up relatively narrow and discrete from the surrounding background. The spectrogram plotting frequency, time, and intensity against one another is very useful for rapid qualitative recognition. This is how passive sonar data is interpreted in a time frequency LOFAR display (Low Frequency Analysis and Ranging). Why is it black though? i.e. low intensity?
Sidebar: if anyone wants me to talk offline (or in here) about why the rays trace like they do and why some of this stuff works I can do that. I say that only because a few people have asked or gotten me on that tangent and said “oh that makes sense now.”

## Slide 18: The path forward
Testing different geometries and power levels
  Optimize settings for discreet chirps vice broadband swaths
  Determine effective and efficient geometries
Build it!
  The University of Kansas will build a test pinger for the Radio Echo Telescope (RET) group

## Slide 19: Info, data, chart sources
Particle-level model for radar based detection of high-energy neutrino cascades
  S Prohira, D Besson: 2017
  https://arxiv.org/abs/1710.02883
Observation of Radar Echoes From High-Energy Particle Cascades
  S. Prohira, K.D. de Vries, P. Allison, J. Beatty, D. Besson, A. Connolly, N. van Eijndhoven, C. Hast, C.-Y Kuo, U.A. Latif, T. Meures, J. Nam, A. Nozdrina, J.P. Ralston, Z. Riesen, C. Sbrocco, J. Torres, S. Wissel: 2019
  https://arxiv.org/abs/1910.12830

## Slide 20: Questions?